## Slide 1
Array of elastic particles in contact with each other.
They present strong nonlinear behavior and solitary waves can exist inside them.
The particle size and Young modulus can be controlled, changing the properties.
What are Granular Crystals?
The input space is high dimensional and the computational cost of finding functions (surrogates) that fit the data grows exponentially.
The optimization problem
A tool for researchers and students
A graphical user interface gives easy access to the surrogates for simulations, and properties.
Conclusions
It is possible to produce error bounds for measurements and have an idea of where the error comes from.
The model is applicable to models of various properties, such as particle size and number of particles.
*Department of Electric and Electronic Engineering, University of Los Andes, Bogota DC, Bogota, 111711, Colombia
†Department of Mechanical Engineering, Purdue University, West Lafayette, Indiana, IN 47907, USA
Juan Lopez*, Rohit Tripathy†, Ilias Bilionis†, Marcial Gonzalez†
Efficient Exploration of Quantified Uncertainty in Granular Materials
Chain Motion
The properties can be defined in terms of the motion of the chain.
Abstract: Granular crystals present unique nonlinear behaviors that support standing waves. These can be controlled through precompression and impurities for different applications, such as impact and shock dissipation, and energy harvesting devices. Even though, the study of granular crystals is relatively new, there exist different models that describe them. As many models in other fields, they rely on particular approximations and suppositions, and experimental results show agreement with them. However there are experimental errors that are not easily accounted for and are usually attributed to some of the approximations made or phenomena that is not considered in the models. The errors observed might be the result of not quantifying uncertainty in the models. This work presents a way of doing uncertainty propagation through the method of active subspaces and Gaussian process regression, in a computationally efficient way.
Future work
One model is available for simulation. Future versions of the tool will include more models and an option to upload personalized models.
These methods can be applied to more complex systems.
References
[1] Gonzalez M., Yang J., Daraio C. and Ortiz M., Mesoscopic approach to granular crystal dynamics, Physical Review E, 85, 016604, 2012.
[2] Yang J., Gonzalez M., Kim E., Agbasi C., and Sutton M., Attenuation of solitary waves and localization of breathers in 1D granular crystals visualized via high speed photography, Experimental Mechanics, 54, 1043–1057, 2014.
[3] Marcial Gonzalez and Alberto M. Cuitiño. A nonlocal contact formulation for confined˜ granular systems. Journal of the Mechanics and Physics of Solids, 60(2):333–350, 2012
[4] Caishan Liu, Zhen Zhao, and Bernard Brogliato. Theoretical Analysis and Numerical Algorithm for Frictionless Multiple Impacts in Multibody Systems. Inria, 2008
[5]C. E. Rasmussen and C-K. Williams, Gaussian processes for machine learning, USA: MIT Press, 2006
[6] [1] Ilias Bilionis and Nicholas Zabaras. Bayesian uncertainty propagation.
Granular chain with beads of different materials and size. (http://www.mechmat.ethz.ch/research.html)
Check condition for collision
Yes
Update variables
Is it in a collision process?
No
Finish
Time-stepping integration of the equations of motion
Reduced inputs
Inputs (sources of uncertainty)
Output (quantities of interest)
Discover and exploit
Active Subspaces
(where response exhibits maximal variability)
Use a Gaussian Process regression as surrogate
Constantine-2013 (math@C.Mines)
Bilionis-2015 (gradient free, reduces to an optimization process)
1D granular chain. There are multiple contacts.
Graphical user interface
Joint plots for different properties in different particles.
Surrogate functions with a confidence interval of 97.5%
Tool available at: https://nanohub.org/tools/gransurrogate
[1][2]